## Slide 1
Group 3:
Bùi Trịnh Thế Viên
Trần Đăng Bách
Nguyễn Văn Quý
Nguyễn Trọng Nhân
Embedded Systems
Restaurant Delivery Robot

## Slide 2
Table of Contents:
  Introduction (overview + objectives)
  System Architecture & Flowchart Diagrams
  Use Case Diagram
  Timeline
  Project Task Allocation (tasks + contribution percentage)

## Slide 3
COMPONENTS
STLINK-V2
MCP2551
Driver motor
Motor N20
Line sensor
ESP32-C3
STM32H5
Resistor-120ohm

## Slide 4
MPU6050
HC-SR04
BUTTON
Pin Li-ion
LM2596
COMPONENTS
PCB
Wheel
Oled(I2C)

## Slide 5
SOFTWARE & DEBUGGING TOOLS
Development IDEs
  STM32CubeIDE
  ESP-IDF
  VS Code + Espressif Extension
Firmware Libraries
  FreeRTOS
  STM32 HAL
  ESP-IDF TWAI driver
  ESP-IDF WiFi + lwIP
  MPU-6050/9250 driver
  SSD1306 driver
  Madgwick / Complementary Filter
Debugging & Analysis Tools
  OpenOCD + GDB
  Saleae Logic Analyzer
  ESP-IDF Monitor
  SEGGER SystemView

## Slide 6
Problem Statement:
In today's context, the restaurant service industry is gradually shifting toward automation in order to:
  Reduce labor costs
  Increase service efficiency
  Enhance customer experience
However, existing restaurant robot systems still have several limitations:
  Centralized processing → prone to overload, difficult to scale
  Slow response in emergency situations
  Lack of stability when operating in real-world environments
Therefore, there is a need to build a robot system that:
  Is capable of distributed processing
  Guarantees real-time performance
  Operates safely and reliably
  Introduction

## Slide 7
This project focuses on designing an automated delivery robot using a Multi-MCU architecture combined with CAN Bus communication.
The system is divided into 3 main blocks:
  MCU1 (ESP32): handles system logic, receives orders via WiFi, and coordinates the overall system
  MCU2 (STM32H5): controls movement, positioning, and navigation
  MCU3 (STM32H5): handles sensor processing and ensures safety
Each microcontroller operates independently and communicates with one another via CAN Bus, which helps to:
  Increase system stability
  Reduce processing load on each block
  Allow easy system expansion
The system uses FreeRTOS to manage multitasking and ensure real-time operation.
  Introduction

## Slide 8
Objectives:
  General Objective:
    To build a restaurant delivery robot system capable of operating autonomously, stably, and safely in a real restaurant environment.
  Specific Objectives:
    Receive and process orders via WiFi connection
    Navigate the robot to the desired destination
    Detect and avoid obstacles in real time
    Perform an emergency stop when a hazard occurs
    Return to the base position after completing a delivery
    Enable communication between MCUs via CAN Bus
    Apply FreeRTOS for efficient multitasking management
  Introduction

## Slide 9
Node | ID
ESP32 | 0x01
STM32H5 | 0x02
STM32H5 | 0x03
  1. System Architecture
System Architecture: 3 nodes on CAN Bus:
  ESP32 (MCU1) — Brain / WiFi / Mission Controller / OLED Display
  STM32H5 (MCU2) — Motion & Navigation Controller
  STM32H5 (MCU3) — Perception & Safety Controller

## Slide 10
Node | ID
ESP32 | 0x01
STM32H5 | 0x02
STM32H5 | 0x03
Message ID Structure (11-bit):
  Bits [10:8] = Sender Node ID
  Bits [7:0] = Message Type
MCU3 (0x3xx) | MCU2 (0x2xx) | Type | MCU1 (0x1xx)
EMERGENCY_STOP → MCU2 | NAV_STATUS → MCU1 | 0x01 | NAV_CMD → MCU2
OBSTACLE_ALERT → MCU1 | ARRIVED → MCU1 | 0x02 | RETURN_BASE → MCU2
PATH_CLEAR → MCU1 | ODOMETRY → MCU1 | 0x03 | SOFT_STOP → MCU2
PERCEPTION_REPORT → MCU1 | BUMP_ALERT → MCU1 | 0x04 | PERCEPTION_ARM → MCU3
HEARTBEAT → MCU1 | HEARTBEAT → MCU1 | 0x05 | HEARTBEAT → ALL
  1. System Architecture

## Slide 11
  2. Flow chart

## Slide 12
  2. Flow chart
ESP32 (MCU1) — Brain, WiFi, Mission Controller, OLED Display

## Slide 13
ESP32 (MCU1) — Brain, WiFi, Mission Controller, OLED Display
State machine task
  2. Flow chart

## Slide 14
STM32H5 (MCU2) — Motion & Navigation Controller
  2. Flow chart

## Slide 15
STM32H5 (MCU2) — Motion & Navigation Controller
  2. Flow chart

## Slide 16
STM32H5 (MCU3) — Perception & Safety Controller
  2. Flow chart

## Slide 17
STM32H5 (MCU3) — Perception & Safety Controller
  2. Flow chart

## Slide 18
  Use case diagram

## Slide 19
  Timeline

## Slide 20
Week 1 — Topic Definition:
  Finalize topic: Service Robot
  Write:
    Problem Statement
    Introduction
    Objectives
  Design:
    Draw system block diagram (3 MCUs)
    List components
  Output:
    Proposal slides
    System diagram
  Timeline
Week 2 — System Design + App/Web
  Embedded DesignSystem architecture design:
    CAN ID table (0x101, 0x102, 0x302…)
    FreeRTOS task design for each MCU
  App / Web DevelopmentBuild a simple web interface:
    Table selection
    Order submission
  ESP32 side:
    HTTP server or WebSocket server
    Receive order → push to queue
  Expected Output:Detailed system architecture diagram
  CAN message table
  Working web application

## Slide 21
  Timeline
Week 3 — Hardware + CAN + Testing
  Hardware Connection:
    ESP32 ↔ STM32 via CAN Bus
  Testing:
    Send command from web app → ESP32 → CAN Bus
    CAN communication verification
    Motor running via PWM
    Expected Output:Motor running successfully
    CAN send/receive verified and working
Week 4 — MOTOR CONTROL + PID:
  Read encoder
  Implement PID:
    Speed control
  Test:
    Move straight
    Turn left/right
  Output:
    Stable robot movement

## Slide 22
Week 5 — SENSOR + NAVIGATION:
  Line sensor:
    Read ADC
    Calculate error
  Ultrasonic sensor:
    Measure distance
  Logic:
    Line following
    Obstacle avoidance
  Output:
    Autonomous robot with obstacle avoidance
  Timeline
Week 6 — Full 3-MCU Integration
  Add MCU3:
    Ultrasonic sensors + emergency stop logic
  Implement:
    Emergency stop via CAN bus
  MCU1:
    State machine implementation
  Expected Output:
    Robot able to:
      Receive commands
      Navigate and move
      Stop when obstacle detected

## Slide 23
  Timeline
Week 7 — Finalization + Demo:
  Debug the entire system
  Prepare:
    Slides
    Report
    Demo video
  Output:
    Complete demo
    Slides + report

## Slide 24
Student | Suggested Tasks | Contribution
Bùi Trịnh Thế Viên | Write problem, introduction, and app concept, Develop web app and ESP32 WiFi communication,Test app → ESP32 → CAN command flow, Send control commands from app, Improve UI, Implement state machine, Finalize web app and demo, design PCB | 25%
Trần Đăng Bách | Research sensors and safety mechanism, Design obstacle detection logic, Test ultrasonic sensors, Support sensor testing and integration, Implement obstacle avoidance, Implement emergency stop, Perform safety testing | 25%
Nguyễn Văn Quý | Design system architecture and motor selection, Design PID and motor control logic, Test motor PWM and encoder reading, Implement PID and test robot movement, Develop navigation and line following, Optimize motor control, Tune robot performance | 25%
Nguyễn Trọng Nhân | Prepare proposal slides and system overview, Design CAN communication and FreeRTOS tasks, Setup and debug CAN communication, Debug timing and system communication, Synchronize data between MCUs, Integrate full system (3 MCUs), Prepare report, slides, and video | 25%